## Slide 1: Protocol “Layers”
Networks are complex!
many “pieces”:
  hosts
  routers
  links of various media
  applications
  protocols
  hardware, software
Question:
Is there any hope of organizing structure of network?
Or at least our discussion of networks?

## Slide 2: Why layering?
Dealing with complex systems:
explicit structure allows identification, relationship of complex system’s pieces
  layered reference model for discussion
modularization eases maintenance, updating of system
  change of implementation of layer’s service transparent to rest of system
  e.g., change in gate procedure doesn’t affect rest of system
layering considered harmful?

## Slide 3: Internet protocol stack
application: supporting network applications
  FTP, SMTP, HTTP
transport: process-process data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  PPP, Ethernet
physical: bits “on the wire”
application
transport
network
link
physical

## Slide 4: ISO/OSI reference model
presentation: allow applications to interpret meaning of data, e.g., encryption, compression, machine-specific conventions
session: synchronization, checkpointing, recovery of data exchange
Internet stack “missing” these layers!
  these services, if needed, must be implemented in application
  needed?
application
presentation
session
transport
network
link
physical

## Slide 5: Encapsulation
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame

## Slide 6: Chapter 1: roadmap
  1.1 What is the Internet?
  1.2 Network edge
    end systems, access networks, links
  1.3 Network core
    circuit switching, packet switching, network structure
  1.4 Delay, loss and throughput in packet-switched networks
  1.5 Protocol layers, service models
  1.6 Networks under attack: security
  1.7 History

## Slide 7: Network Security
attacks on Internet infrastructure:
  infecting/attacking hosts: malware, spyware, worms, unauthorized access (data stealing, user accounts)
  denial of service: deny access to resources (servers, link bandwidth)
Internet not originally designed with (much) security in mind
  original vision: “a group of mutually trusting users attached to a transparent network” 
  Internet protocol designers playing “catch-up”
  Security considerations in all layers!

## Slide 8: What can bad guys do: malware?
Spyware:
  infection by downloading web page with spyware
  records keystrokes, web sites visited, upload info to collection site
Virus
  infection by receiving object (e.g., e-mail attachment), actively executing
  self-replicating: propagate itself to other hosts, users
Worm:
  infection by passively receiving object that gets itself executed
  self- replicating: propagates to other hosts, users
Sapphire Worm: aggregate scans/sec
in first 5 minutes of outbreak (CAIDA, UWisc data)

## Slide 9: Denial of service attacks
attackers make resources (server, bandwidth) unavailable to legitimate traffic by overwhelming resource with bogus traffic
select target
break into hosts around the network (see malware)
send packets toward target from compromised hosts
target

## Slide 10: Sniff, modify, delete your packets
Packet sniffing:
  broadcast media (shared Ethernet, wireless)
  promiscuous network interface reads/records all packets (e.g., including passwords!) passing by
A
B
C
src:B dest:A payload
  Ethereal software used for end-of-chapter labs is a (free) packet-sniffer
  more on modification, deletion later

## Slide 11: Masquerade as you
IP spoofing: send packet with false source address
A
B
C
src:B dest:A payload

## Slide 12: Masquerade as you
IP spoofing: send packet with false source address
record-and-playback: sniff sensitive info (e.g., password), and use later
  password holder is that user from system point of view
A
B
C
src:B dest:A user: B; password: foo

## Slide 13: Masquerade as you
IP spoofing: send packet with false source address
record-and-playback: sniff sensitive info (e.g., password), and use later
  password holder is that user from system point of view
A
B
later …..
C
src:B dest:A user: B; password: foo

## Slide 14: Network Security
more throughout this course
chapter 8: focus on security
crypographic techniques: obvious uses and not so obvious uses