## Slide 1: Chapter 5: The Data Link Layer
Our goals:
understand principles behind data link layer services:
  error detection, correction
  sharing a broadcast channel: multiple access
  link layer addressing
  reliable data transfer, flow control: done!
instantiation and implementation of various link layer technologies

## Slide 2: Link Layer
5.1 Introduction and services
5.2 Error detection and correction
5.3Multiple access protocols
5.4 Link-layer Addressing
5.5 Ethernet
5.6 Link-layer switches
5.7 PPP
5.8 Link virtualization: ATM, MPLS

## Slide 3: Link Layer: Introduction
Some terminology:
hosts and routers are nodes
communication channels that connect adjacent nodes along communication path are links
  wired links
  wireless links
  LANs
layer-2 packet is a frame, encapsulates datagram
data-link layer has responsibility of
transferring datagram from one node
to adjacent node over a link

## Slide 4: Link layer: context
datagram transferred by different link protocols over different links:
  e.g., Ethernet on first link, PPP on intermediate links, 802.11 on last link
each link protocol provides different services
  e.g., may or may not provide reliable data transfer over link
transportation analogy
trip from Princeton to Lausanne
  limo: Princeton to JFK
  plane: JFK to Geneva
  train: Geneva to Lausanne
tourist = datagram
transport segment = communication link
transportation mode = link layer protocol
travel agent = routing algorithm

## Slide 5: Link Layer Services
framing, link access:
  encapsulate datagram into frame, adding header, trailer
  channel access if shared medium
  “MAC” addresses used in frame headers to identify source, dest
    different from IP address!
reliable delivery between adjacent nodes
  we learned how to do this already (chapter 3)!
  seldom used on low bit-error link (fiber, some twisted pair)
  wireless links: high error rates
    Q: why both link-level and end-end reliability?

## Slide 6: Link Layer Services (more)
flow control:
  pacing between adjacent sending and receiving nodes
error detection:
  errors caused by signal attenuation, noise.
  receiver detects presence of errors:
    signals sender for retransmission or drops frame
error correction:
  receiver identifies and corrects bit error(s) without resorting to retransmission
half-duplex and full-duplex
  with half duplex, nodes at both ends of link can transmit, but not at same time

## Slide 7: Where is the link layer implemented?
in each and every host
link layer implemented in “adaptor” (aka network interface card NIC)
  Ethernet card, PCMCI card, 802.11 card
  implements link, physical layer
attaches into host’s system buses
combination of hardware, software, firmware
controller
physical
transmission
cpu
memory
host
bus
(e.g., PCI)
network adapter
card
host schematic
application
transport
network
link
link
physical

## Slide 8: Adaptors Communicating
sending side:
  encapsulates datagram in frame
  adds error checking bits, rdt, flow control, etc.
receiving side
  looks for errors, rdt, flow control, etc
  extracts datagram, passes to upper layer at receiving side
controller
controller
sending host
receiving host
datagram
datagram
datagram
frame

## Slide 9: Link Layer
5.1 Introduction and services
5.2 Error detection and correction
5.3Multiple access protocols
5.4 Link-layer Addressing
5.5 Ethernet
5.6 Link-layer switches
5.7 PPP
5.8 Link Virtualization: ATM. MPLS

## Slide 10: Error Detection
EDC= Error Detection and Correction bits (redundancy)
D = Data protected by error checking, may include header fields
Error detection not 100% reliable!
  protocol may miss some errors, but rarely
  larger EDC field yields better detection and correction
otherwise

## Slide 11: Parity Checking
Single Bit Parity:
Detect single bit errors
Two Dimensional Bit Parity:
Detect and correct single bit errors
0
0

## Slide 12: Internet checksum (review)
Sender:
treat segment contents as sequence of 16-bit integers
checksum: addition (1’s complement sum) of segment contents
sender puts checksum value into UDP checksum field
Receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  NO - error detected
  YES - no error detected. But maybe errors nonetheless?
Goal: detect “errors” (e.g., flipped bits) in transmitted packet (note: used at transport layer only)

## Slide 13: Checksumming: Cyclic Redundancy Check
view data bits, D, as a binary number
choose r+1 bit pattern (generator), G
goal: choose r CRC bits, R, such that
  <D,R> exactly divisible by G (modulo 2)
  receiver knows G, divides <D,R> by G. If non-zero remainder: error detected!
  can detect all burst errors less than r+1 bits
widely used in practice (802.11 WiFi, ATM)

## Slide 14: CRC Example
Want:
  D.2r XOR R = nG
equivalently:
  D.2r = nG XOR R
equivalently:
if we divide D.2r by G, want remainder R
R = remainder[ ]
D.2r
G
Notes: Remember subtraction = addition = XOR